Sound Beats

# Introduction

When two sound waves with different but close frequencies interfere with each other, what is heard is a sound whose frequency is the average of the two original frequencies. This sound varies in intensity and the variations in intensity have a frequency that is equal to the difference between the two original frequencies.

If the original waves are:

y1 =A sin( 2( f1 t )	,	y2 = A sin( 2( f2 t )

Where f1, f2 are the frequencies, than the composite wave will be of the form:

y = 2A cos( 2( (f1 - f2) t) sin(2( (f1 + f2) t)

in this experiment we explore the form of the composite wave by viewing the readings of a microphone and by looking at the Fourier transform of these readings.

# Equipment List

Datalogger interface connected to a PC

Two tuning forks mounted on sounding boxes (frequencies: 440Hz, 435Hz)

A rubber hammer to sound the forks

Sound sensor

Procedure

## 1.  Connect the circuit as shown in Figure 1.

## -Figure 1-

## 2.  Connect the sound sensor to a socket on the interface.

## 3. Hit one of the tuning forks with the rubber hammer. Wait for a few seconds for the high-pitched to subside.

## 4. While the fork is still sounding, start the software to collect data.

## 5. Save the results.

## 6. Repeat steps 1 to 3 with the other tuning fork. Remember to save the collected data under a different file name.

## 7. Repeat steps 1 to 3 while sounding both forks simultaneously. Save the results under a new file name.

## Analysis

1.  Describe what you hear while sounding both tuning forks simultaneously.

2.  Describe the 3 graphs generated and give explanations for your results.

3. If we replace one of the tuning forks to a higher frequency (for example: 480Hz), what can you hear?

4. Is there any difference in the graph generated?